## Slide 1
Karl Lautenschläger
Suitability of Modern Wi-Fi for Wireless Infield-Communication
Final Thesis
Notes: My Name is
I'm studying Information System Engineering in my kind of Masters at the TU Dresden
Start final thesis in November
<number>
2/8/23

## Slide 2: Agenda
Motivation Final Thesis
Physical Layer Technologies
Field Measurements
Simulation Experiments

## Slide 3
<number>
Modern Wi-Fi
 | IEEE 802.11ac (Wi-Fi 5) | IEEE 802.11ax (Wi-Fi 6)
Spectrum | 5 GHz | 2.4 GHz, 5 GHz
Bandwidth | Up to 160 MHz | Up to 40 Mhz (2.4 GHz), 160 Mhz at 5 GHz
OFDM Guard Interval | 0.4 or 0.8 μs | 0.8, 1.6 or 3.2 μs
Maximal Data Rate | 6.9 Gbit/s | 9.6 Gbit/s
Max Modulation Coding Scheme | 256-QAM | 1024-QAM
Multi-User Technology | MU-MIMO | MU-MIMO, OFDMA
Multi-User Transmission Direction | Downlink | Downlink und Uplink
K. Lautenschlaeger, Suitability of Modern Wi-Fi for Wireless Infield-Communication
Notes: Of course better Data Rate
Multi user? Stadium
Because when to many people want to
But Amendments for improving outdoor communication
But indoor and outdoor range in the agriculture domain is unknown
<number>

## Slide 4
Physical Layer Technologies

## Slide 5: Physical Layer Technologies
OFDM Guard Interval
Low density parity check
Dual Carrier Modulation
Extended Range Mode
Multiple Input Multiple Output
Space-Time-Block-Codes
Bandwidth
...
Notes: Modulation Coding Scheme
New Error correction codes
Transmission power
Any questions so far?
What is possible?
What do we need? How bad are shadowing effect multipath effects?
Dave Smart getting in touch with the chips companies?

## Slide 6
Throughput
Robustness
Range
Notes: Modulation Coding Scheme
New Error correction codes
Transmission power
Any questions so far?
What is possible?
What do we need? How bad are shadowing effect multipath effects?
Dave Smart getting in touch with the chips companies?

## Slide 7: Modern Wi-Fi
Wi-Fi 6
(802.11ax):
  4 MIMO Streams
  2.4 GHz and 5 GHz
  STBC
  DCM
  Extended Range Mode
  LDPC
  Bandwidth(20-160 MHz)
802.11bd:
  1 Stream
  5.9 Ghz
  DCM
  Extended Range
  LDPC
  Bandwidth(10-20)

## Slide 8
K. Lautenschlaeger, Suitability of IEEE 802.11ax \ IEEE 802.11ac for Wireless Infield-Communication
<number>
Simulation
Harvest Platooning Service
Notes: Physical Layer amendment of Wifi 6
Longer Preamble for extended range
Next transporting machine waiting in line
Simulate such a system
3-5 Harvest Platoons on a field?
<number>

## Slide 9: Simulation Harvest Platooning Service

## Slide 10: Simulation Harvest Platooning Service

## Slide 11: Simulation Harvest Platooning Service

## Slide 12: Simulation Harvest Platooning Service

## Slide 13: Simulation Harvest Platooning Service

## Slide 14: Simulation Harvest Platooning Service

## Slide 15: Simulation Harvest Platooning Service

## Slide 16
K. Lautenschlaeger, Suitability of IEEE 802.11ax \ IEEE 802.11ac for Wireless Infield-Communication
<number>
Simulation
Agricultural Platooning Service in Leader-Follower-Scenario
Leader
Follower_1
Follower_2
Notes: <number>

## Slide 17
Field Measurements

## Slide 18
K. Lautenschlaeger, Suitability of IEEE 802.11ax \ IEEE 802.11ac for Wireless Infield-Communication
<number>
Summary
Analyzing Telemetry data of Use Cases
  required latency
  required data Rate
  required communication distance
Field measurements
  communication range
  received signal strength in agricultural scenarios
  Latency
Simulation
  Leader-Follower-Scenario
  Harvest-Platoon-Scenario
Notes: Recall interest in the topic Advice, recommendations,
Cooperate work together
Frame of a final thesis, support the group

## Slide 19
Thanks!
Notes: <number>
2/8/23